## Slide 2: Smart Graincam
CNH Industrial
Paul Snauwaert

## Slide 3: CNHi STRATEGY: Fully automated combines
  END GOAL OF THE GRAIN CAM PROJECT
  Automatically adjust the functional parameters of the combine
  EXPECTED RESULT
  Maximized throughput
  Frees up time for the operator to focus on other things (e.g. unload on the go, mapping, feeding, harvest management …)
  Results in stress free harvesting
  Makes it easier to find operators

## Slide 4: CNHi STRATEGY: Fully automated combines
  Challenge
  Sense the internal state of the combine process, e.g. grainquality
Sieve loss
Rotor loss
Returns volume
Engine load
Inclination sensors
Sieve load
Yield and moisture
Feed rate sensor
Rotor vanes angle
22” models only
Graincam

## Slide 5
SMART GRAIN CAM: The current state
  Camera
  A multispectral camera
  Goal
  Assess grain-sample quality

## Slide 6
Wheat
Canola
Corn
Soybeans
Developed and tuned using state of the art image processing techniques
Barley
Rice
+ many others (sunflower, oats , grass seed, peas, ….)
?
  Challenges
  Creating & tuning algorithms able to identify impurities in a wide variety of crops – varieties – conditions
SMART GRAIN CAM: The current state

## Slide 7
PROJECT SMART GRAINCAM: Deep learning powered Grain Cam
  Limitations of current Grain Cam
  The previously used state-of-the-art image processing techniques took long development time
Small set of images (not representative)
Basic algorithm
More images are being collected
A lot of effort needed to update / improve the algorithm
  Limited complexity
Canola  straight forward
Broken kernels –> extremely challenging
  Reasons to switch to AI
  Non-safety critical
    Making a mistake is not such a problem
    Not necessary to understand why the algorithm is detecting certain features
  Shorter iteration times
    Key is the creation of a database of images including enough variability and labeling them
    Retraining if a new situation has been encountered
  More complex features can be identified
    Features that state of the art image processing techniques could never detect

## Slide 8
PROJECT SMART GRAINCAM: Deep learning powered Grain Cam
  PROOF OF CONCEPT
  Demonstrate the power of AI on the barley use-case
PHASE 1
PHASE 2
PHASE 3
  Develop a Barley model that can identify needles
  Develop a Barley model that can identify needles, straw, broken kernels, needles attached to kernels
  Optimize model to run on existing Grain Cam platform, i.e. freescale IMX6 quad core without powerful GPU, in under 4 sec

## Slide 9
PROJECT SMART GRAINCAM: Deep learning powered Grain Cam
  RESULTS
  Multiple models created each with their own strengths & weaknesses
PHASE 1
PHASE 2
PHASE 3
  The selected model was optimized to run on the IMX6 Platform

## Slide 10
  LEARNINGS
  AI methodology is 100% suited for this type of application
  Current effort is focused too much on optimizing the networks for a sub optimal run time environment
PROJECT SMART GRAINCAM: Learnings & next steps
  NEXT STEPS
  Finish Barley use case on existing platform
  Identify future proof platform
    GPU´s vs FPGA